## Slide 1
Load campaign-specific parameters
For each data file:
  Create folder
  Import the .P data file
  Modify config file
  Extract profiles
  Calibrate FP07
  For each profile: run ODAS turbulence analysis (shear)
  Computes corrected conductivity, salinity and density
  For each profile: run Piccolroaz analysis (shear + FP07)
  Save the data
analyze_profiles.m
Contains parameters required for the analysis, dependent on the instrument type, instrument configuration and field campaign.
load_parameters_lakename.m
Level0/VMPxxx.P
Level2/VMPxxx_.../results_VMPxxx.mat
Copy of odas_p2mat with printing option: imports data from .P file.
odas_p2mat_print.m
Main analysis script
Data files
Customized scripts in microstructure folder
ODAS scripts
Copy of read_odas with printing option
read_odas_print.m
Create a copy of the .P data file with updated config parameters (shear sensitivities +pressure offset) from specified .cfg file or from specified parameters.
Import the modified .P file.
get_config.m
Extract .cfg file from a .P data file.
extract_setupstr.m
Patch a .cfg file into a .P data file.
patch_setupstr.m
Extract the profiling indices.
get_profile.m
Perform FP07 calibration.
Patch the modified .cfg file to the .P file.
Import the calibrated .P file.
run_calibration_FP07.m
Modified version of cal_FP07_in_situ: uses temperature from CTD to correct temperature from FP07 and save calibration parameters to .cfg file.
cal_FP07_in_situ_EPFL.m
Runs basic turbulence analysis from shear probes.
quick_look.m
Computes corrected conductivity, salinity and density for a given lake.
compute_rho_salinity.m
Computes pressure with respect to atmospheric pressure and depth
correct_pressure.m
Computes turbulence estimates from shear probes and FP07 based on Piccolroaz et al. (2021).
resolve_turbulence.m

## Slide 2
resolve_turbulence.m

## Slide 3
Other ODAS functions
odas_p2mat.m
read_odas.m